## Slide 1: ECOS03 – Embedded Operational Systems
Rodrigo Maximiano Antunes de Almeida
rmaalmeida@gmail.com
@rmaalmeida
Universidade Federal de Itajubá

## Slide 2: Schedule
1 - Introdução à SO e arquitetura de computadores
2 - Ponteiros, structs, Buffer circulares e ponteiros de função
3 - Processos e schedulers (temporização e prioridade)
4 - Acesso ao hardware via software e interrupções
5 - Device drivers e Controladora de drivers
6 - Gestão de tasks e memória em um sistema operacional
7 - Comunicação interprocessos e criação de um softwatchdog system
8 - Visão geral de sistemas operacionais – Introdução; Estruturas de sistemas operacionais.
9 - Processos – Threads; Sincronização de Processos.
10 - Memória – Memória principal; Memória Virtual
11 - Sistema de Arquivos - Estrutura de memória secundária
12 - Sistemas com múltiplos processadores
13 - Segurança

## Slide 3: The OS

## Slide 4: What is a kernel?

## Slide 5: What is a kernel?

## Slide 6: What is a kernel?
Kernel tasks:
  Manage and coordinate the processes execution using “some criteria”
  Manage the free memory and coordinate the processes access to it
  Intermediate the communication between the hardware drivers and the processes

## Slide 7: What is a kernel?
I/O
CPU
Memory
Kernel
Drivers
Extra libs
File system
Context switch
GUI
C/C++
libraries
Interface actions
System logic
Internal routines

## Slide 8: Develop my own kernel?
Why?

## Slide 9: Develop my own kernel?
Improve home design
Reuse code more efficiently
Full control over the source
Specific tweeks to the kernel
  Faster context switch routine
  More control over driver issues (interrupts)

## Slide 10: Develop my own kernel?
Why not?

## Slide 11: Develop my own kernel?
Kernel overhead (both in time and memory)
Free and paid alternatives
Time intensive project
Continuous development

## Slide 12: Kernel Project
Source code size (millions of lines)
  FreeBSD – 8.8
  IOS – 80
  Linux (2.6.0) – 5.2
  Linux (3.6) – 15.9
  Debian 7.0 – 419
  Mac OS X 10.4 – 86
  OpenSolaris – 9.7
  Windows NT – 11
  Windows XP – 45
  Windows Vista – 66

## Slide 13: Develop my own kernel?
Alternatives
  Windows Embedded Compact®
  VxWorks®
  X RTOS®
  uClinux
  FreeRTOS
  BRTOS

## Slide 14: Electronic building
Electronics review
  Schematics
  Datasheets
  Protoboard/breadboard
  LED
  Potentiometer
  LCD
  Microcontroller
System design
  Basic steps

## Slide 15: Electronics review
http://xkcd.com/730/

## Slide 16: Schematics
Way to represent the components and its connections
Each component has its own symbol
Crossing wires only are connected if joined with a dot

## Slide 17: Circuits 101
Voltage, current, resitance

## Slide 18: Advanced components

## Slide 19: Datasheets
The main source of information concerning electronics
Presents
  Electrical characteristics
  Simplified schematics
  Use example
  Opcodes/API

## Slide 20: LED

## Slide 21: LED

## Slide 22: Potentiometer
Linear/Log
Used as voltage divisor
Need an analog input
Filter

## Slide 23: Potentiometer

## Slide 24: LCD Display

## Slide 25: LCD Display
Complete interface solution
  Screen + Video card + Protocol + Data cable
“Standart” HD44780
  4/8 bits communication
  3 control bits

## Slide 26: LCD Display

## Slide 27: LCD Display
Data connection
Backlite
Current consumption
Power on time/routine

## Slide 28: Microcontroller
System-on-a-chip
  Processor
  Memory
  Input/Output peripherals
  Communication
  Safety components

## Slide 29: Microcontroller
Xtal configuration
Reset pin
DC needs
Many peripherals on the same pin

## Slide 30: System design
Steps on a generic electronic system design
  Define the objective(s)
  Choose the main components needed to achieve the objective
  Get the use example and recommendations from component datasheet
  Build the schematics
  Simulation of HW elements
  Board layout

## Slide 31: System design
Cad tool: KiCAD

## Slide 32: Programming 101
Embedded Tools

## Slide 33: Board programming
Programmer
IDE
Basic concepts
  CPU Architecture
  HW configuration
  Memory access
First program (He110 DEFC0N)
Peripheral setup
Second program (ADC read)

## Slide 34: Board programming
Programmer
  PICkit3
  Can use ICSP
  Can program a lot of Microchip products
  Also a debugger

## Slide 35: Board programming

## Slide 36: Board programming
IDE
  MPLABX
    Based on Netbeans
Compiler
  XC8

## Slide 37: Processor architecture

## Slide 38: 1. Pointers
https://xkcd.com/138/

## Slide 39: Pointers
They are variables that store the address (location) of memory.
  In these memory addresses it is possible to enter values.
The type of the value placed in the memory pointed by the address is defined in the declaration of the pointer.
  The type that tells the compiler how much memory is needed to store the values.
A pointer variable points to a variable of a certain type (char, int, float, double, ...).

## Slide 40: Pointers
It is necessary in the declaration of a pointer, to specify for which type of variable it will point.
Pointers are declared with a * before the variable name.
Sintax:
type *variableName;

## Slide 41: Pointers
int *aux;
float *temp;
char *pont;
aux, temp, and pont are variables that store memory addresses and not variable of the types int, float, or char.
* is used when you want to access the value that is in the memory location and not the memory address.

## Slide 42: Pointers

## Slide 43: Pointers
Operator &:
  Always gets the address of a variable
  Since pointers are also variables, they also occupy memory.
  You can get the pointer address and have pointers to pointers (multiples *).
Operator *:
  The * operator does the opposite of the & operator.
  Given a pointer, the * operator accesses the content pointed to by it.

## Slide 44: Pointers
Operator &:
  “get the address of”
  “saved in”
Operator *:
  “dereference”
  “through”
  “pointed by”

## Slide 45: Pointers
#include <stdio.h>
int main(int argc, char *argv[]){
int x=10;
int *p1=&x; //ponteiro para um inteiro
printf("x = %d\n\n", x);
*p1=20; //ou p1[0]=20;
printf("p1 = %u\n", p1);
printf("x = %d\n", x);
printf("*p1 = %d\n", *p1);
printf("p1[0] = %d\n\n", p1[0]);
return 0;
} //end main

## Slide 46: Parameter passing
C-language functions can receive multiple parameters and can return one.
The method of sending the parameters can be done through the stack or through registers.
The stack allows several parameters to be passed at once
The registers have a lower overhead, therefore being faster and with smaller code size

## Slide 47: Parameter passing
When sending, the parameters are copied to a temporary variable, so that changes in its value are lost after the end of the function.
The initial variable is not changed
To avoid this situation it is common to pass the parameter by reference.
When passing by reference, the address of the variable is passed instead the value. Therefore the function can change the value of the original variable.

## Slide 48: Parameter passing
void incrementa(int a){
a += 1;
}
int main(int argc, char *argv[]){
int x = 10;
incrementa(x);
return 0;
}

## Slide 49
void main(void){
int x = 10;
incrementa(x);
return 0;
}
void incrementa(int a){
a+=1;
return;
}
Rotina Principal
Função

## Slide 50
void main(void)
{
int x = 10;
inc(x);
return 0;
}
void inc(int a){
a += 1;
return;
}
Rotina Principal
Função
Variáveis
x=10

## Slide 51
Rotina Principal
Função
Variáveis
x=10
temp=10
void main(void)
{
int x = 10;
inc(x);
return 0;
}
void inc(int a){
a += 1;
return;
}

## Slide 52
Rotina Principal
Função
Variáveis
x=10
a=10
void main(void)
{
int x = 10;
inc(x);
return 0;
}
void inc(int a){
a += 1;
return;
}

## Slide 53
Rotina Principal
Função
Variáveis
x=10
a=11
void main(void)
{
int x = 10;
inc(x);
return 0;
}
void inc(int a){
a += 1;
return;
}

## Slide 54
Rotina Principal
Função
Variáveis
x=10
descartado
void main(void)
{
int x = 10;
inc(x);
return 0;
}
void inc(int a){
a += 1;
return;
}

## Slide 55
void incrementaptr(int* a){
(*a) += 1;
}
int main(int argc, char *argv[]){
int x = 10;
incrementaptr(&x);
return 0;
} //end main

## Slide 56
void main(void)
{
int x = 10;
incptr(&x);
return 0;
}
void incptr
(int* a){
(*a) += 1;
return;
}
Rotina Principal
Função
Variáveis
x=10

## Slide 57
Rotina Principal
Função
Variáveis
x=10
temp=&x
void main(void)
{
int x = 10;
incptr(&x);
return 0;
}
void incptr
(int* a){
(*a) += 1;
return;
}

## Slide 58
Rotina Principal
Função
Variáveis
x=10
a=&x
void main(void)
{
int x = 10;
incptr(&x);
return 0;
}
void incptr
(int* a){
(*a) += 1;
return;
}

## Slide 59
Rotina Principal
Função
Variáveis
x=11
a=&x
*
void main(void)
{
int x = 10;
incptr(&x);
return 0;
}
void incptr
(int* a){
(*a) += 1;
return;
}

## Slide 60
Rotina Principal
Função
Variáveis
x=11
descartado
void main(void)
{
int x = 10;
incptr(&x);
return 0;
}
void incptr
(int* a){
(*a) += 1;
return;
}

## Slide 61: Parameter passing
Passing parameters by reference allows a function to "return" more than one parameter at a time.
This is done by passing a variable via reference so that the function can write to it.

## Slide 62
//a e b são dados de entrada
//d e r são dados de saída
void div(int a, int b, int* d, int* r){
(*d) = a / b;
(*r) = a % b;
return;
}
void main(void){
int d, r;
div(10, 3, &d, &r);
//d = 3 e r = 1;
return;
}

## Slide 63: 2. Struct

## Slide 64: Struct
// struct declaration
typedef struct{
unsigned short int age;
char name[51];
float weight;
}people;
Structs are composed variables.
Group lots of information as if they were one single variable.
A vector that each position stores a different type

## Slide 65: Struct
void main(void){
people someone = {26, "Name", 70.5};
someone.age = 27;
//using each variable from the struct
printf("Age: %d\n", someone.age);
printf("Name: %s\n", someone.name);
printf("Weight: %f\n", someone.weight);
return 0;
}

## Slide 66: Struct
typedef struct{
char nome[20];
int idade;
int *p_dado;
}t_aluno;
t_aluno *a1;
(*a1).idade = 18;
a1->idade = 18;
The access of the internal members of structures, pointed by pointers, can actually be done through the operator ->

## Slide 67: Struct
void main(void){
int dado = 10;
t_aluno aluno = {"Nome",17,&dado};
t_aluno *a1;
a1 = &aluno;
(*a1).idade = 18;
printf("Age: %d\n", (*a1).idade);
a1->idade = 19;
printf("Age: %d\n", a1->idade);
*(aluno.p_dado) = 11;
printf("dado: %d\n", dado);
//aluno->p_dado = 12; //erro
//printf("dado: %d\n", dado);
*((*a1).p_dado) = 12;
printf("dado: %d\n", dado);
*(a1->p_dado) = 13;
printf("dado: %d\n", dado);
return 0;
}

## Slide 68: 3. Circular buffers

## Slide 69: Circular Buffers
“Endless” memory spaces
Use FIFO aproach
Store temporary data
Can implemented using vectors or linked-lists

## Slide 70: Circular Buffers
Vector implementation
  Uses less space
  Need special caution when cycling
  Problem to differentiate full from empty

## Slide 71: Circular Buffers
[0]
[1]
[2]
[3]
[4]

## Slide 72: Empty buffer
[0]
[1]
[2]
[3]
[4]
end=0
start=0
?
?
?
?
?

## Slide 73: Adding 2 elements
[0]
[1]
[2]
[3]
[4]
end=2
start=0
A
B
?
?
?

## Slide 74: Removing 1 element
[0]
[1]
[2]
[3]
[4]
end=2
start=1
A
B
?
?
?

## Slide 75: Adding 2 elements
[0]
[1]
[2]
[3]
[4]
end=4
start=1
A
B
C
D
?

## Slide 76: Adding 1 element
[0]
[1]
[2]
[3]
[4]
end=0
start=1
A
B
C
D
E

## Slide 77: Circular buffers
#define CB_SIZE 10
int circular_buffer[CB_SIZE];
int index=0;
for(;;){
//do anything with the buffer
circular_buffer[index] = index;
//increment the index
index = (index+1)%CB_SIZE;
}

## Slide 78: Circular buffers
#define CB_SIZE 10
int circular_buffer[CB_SIZE];
int start=0, end=0;
char AddBuff(int newData)
{
//check if there is space to add a number
if ( ((end+1)%CB_SIZE) != start)
{
circular_buffer[end] = newData;
end = (end+1)%CB_SIZE;
return SUCCESS;
}
return FAIL;
}

## Slide 79: Exercise
Implement a circular buffer
  Use a 10-position vector
Each element of the vector is a structure with two variables
  char * ProcessName;
  int Time;
Create one function to add new elements and one to remove the oldest elements.

## Slide 80: Exercise
//definição da estrutura
typedef struct {
char* nome;
int time;
}process;
//definição do buffer circular
#define BUFFERSIZE 10
process buffer[BUFFERSIZE];
//definição dos “ponteiros” de acesso
int start, end;

## Slide 81: Exercise
//função de adição de “process” no buffer
void addProc(char *nnome, int ntime){
//checagem de espaço disponível
if ( ((end+1)%BUFFERSIZE) != start){
//Atualização da posição atual
buffer[end].nome = nnome;
buffer[end].time = ntime;
//incremento da posição
end = (end+1)%(BUFFERSIZE);
}
}

## Slide 82: Exercise
//função de remoção de um “process” do buffer
void removeProc (void){
//checagem se existe alguem pra retirar
if (end != start){
//incremento da posição
start = (start +1)%(BUFFERSIZE);
}
}

## Slide 83: Exercise
#include "stdio.h"
void main (void){
addProc("proc1", 0);
addProc("proc2", 1);
addProc("proc3", 2);
removeProc();
removeProc();
removeProc();
}

## Slide 84: 4. Function pointers

## Slide 85: Problem
How to execute a function that is not known at compile time?
  Know the address of the function at runtime.
  Stack the parameters correctly that the function needs
  Make a function call to this address

## Slide 86: Function pointers
Work almost as a normal pointer
Its manipulation obeys all pointer manipulation rules.
Hold the address of a function start point instead the address of a variable
The compiler need no known the function signature to pass the correct parameters and the return value.
Awkard declaration (it is best to use a typedef)

## Slide 87: Function pointers
//defining the type pointerTest
//it is a pointer to function that:
// receives no parameter
// returns no parameter
typedef void (*pointerTest)(void);
//Function to be called
void nop (void){ __asm NOP __endasm }
//creating an pointerTest variable;
pointerTest foo;
foo = nop;
(*foo)(); //calling the function via pointer

## Slide 88: Software engines

## Slide 89: Software engines
Necessity:
  Make an image editor that can choose the right function to call
1st Implementation
  Use a option parameter as a switch operator

## Slide 90: Software engines
image Blur(image nImg){}
image Sharpen(image nImg){}
image imageEditorEngine(image nImg, int opt){
image temp;
switch(opt){
case 1:
temp = Sharpen(nImg);
break;
case 2:
temp = Blur(nImg);
break;
}
return temp;
}

## Slide 91: Soft.Eng. v2
Re-code the image editor engine using function pointers

## Slide 92: Function pointers
image Blur(image nImg){}
image Sharpen(image nImg){}
typedef image (*ptrFunc)(image nImg);
//image editor engine
image imageEditorEngine(ptrFunc function,
image nImg){
image temp;
temp = (*function)(nImg);
return temp;
}

## Slide 93: Function pointers
Good
  New function additions do not alter the engine
  The engine only needs to be tested once
  Can change the function implementations dynamically
Bad
  More complex code (function pointers are not easy to understand for beginners)
  Probable bugs
  Lack of compile time guarantees (function signature)
  Problems with branch predictor

## Slide 94: Exercise
Using function pointers